## Slide 1
COMP6841 PROJECT
Signal Forge CTF
A sim-first contested spectrum training lab with real cyber-security progression
RF visibility -> protocol analysis -> backend abuse -> reverse engineering -> firmware, HDL and jamming resilience
Lab principle
No SDR hardware required
GNU Radio remains editable
Signals and cyber faults are local
Advanced tasks point toward SOTA practice
SIGNAL FORGE CTF
01

## Slide 2
The training gap is the trust boundary between RF and software
Learners often see RF, web exploitation, firmware, and hardware security as separate worlds. This CTF makes them one investigation.
SIGNAL FORGE CTF
02
What beginners see
A waterfall has energy
A packet carries text
A backend returns a quote
What defenders need
Signal confidence has limits
Decoded fields are untrusted input
Operational effects need policy
What the CTF teaches
Observe, tune, decode
Attack controlled local systems
Compare secure designs
The core lesson is not “break a radio”; it is “never trust RF-origin data just because it arrived through a familiar system.”

## Slide 3
The experience is structured as situations, not loose tasks
Each context contains small subtasks with a flag, a story, signal evidence, radio controls, hints, and a safe local success condition.
SIGNAL FORGE CTF
03
6
training situations
22
subtasks with flags
2
advanced contexts
8
GNU Radio-backed generated replays
Learner loop
inspect signal
operate receiver
decode/reverse
trigger local effect
submit flag
The page now treats contexts as the visible situations; subtasks live inside each context page so the structure matches the spreadsheet specification.

## Slide 4
The architecture keeps the lab safe while preserving technical depth
The assessed path is local and synthetic; developer hooks can still connect real GNU Radio work and external scripts.
SIGNAL FORGE CTF
04
GNU Radio .py
Editable flowgraphs define vector payloads, bit packing, repeat timing and carrier tone.
Python backend
Synthesizes looping cf32 IQ, FFT rows, parser events, raw samples and flag checks.
Browser workbench
Waterfall, time series, cursors, zoom, pause/play, task hints and submissions.
Learner scripts
Terminal commands, TCP ingest and ZMQ bridge support external automation.
SQLite and local APIs
Vulnerable and safe endpoints support SQLi, logic flaws and defensive comparison.
Challenge data
Contexts, subtasks, artifacts, hints and validation remain structured JSON.
No transmit-capable workflow is required for solving; live radio integration remains a developer extension.

## Slide 5
The challenge ladder ramps from visible signals to serious cross-domain attacks
The first contexts teach RF operations; the later contexts force reverse engineering, binary exploitation, HDL review, spoofing, and jamming reasoning.
SIGNAL FORGE CTF
05
Context
Level
Tasks
Points
Skill focus
Tunnel Infrastructure
Basic
4
490
signals + cema
Broadcasting Song Metadata
Basic
4
490
signals + cema + cyber
Weather Broadcast Boring Voice
Moderate
3
680
signals + cyber
Civilian Emergency Audio Network
Moderate
3
700
signals + cyber
Bushfire C2
Advanced
4
1440
cyber + cema
Farm Gates
Advanced
4
1440
cyber + cema

## Slide 6
GNU Radio is now the editable source of signal truth
The site no longer depends on recordings as the default. It reads generated Python flowgraphs and synthesizes repeatable IQ streams for the UI.
SIGNAL FORGE CTF
06
Vector source
payload bytes
MSB unpack
8 bits per byte
Repack
1 or 2 bits/symbol
Repeat
symbol timing
Carrier
10 kHz tone
Current working examples
Tunnel tasks: OOK/ASK amplitude, 500 samples per symbol
Song metadata: 4-level ASK, 2 bits per symbol, MSB order
Why this matters
Change C/Python/GNU Radio files and reload
Keep captured recordings as optional evidence snapshots

## Slide 7
Cyber depth is woven through the RF story
The project starts with backend exploitation and grows into reverse engineering, binary exploitation, firmware, HDL and operator-console trust failures.
SIGNAL FORGE CTF
07
SQLi + logic
RF-derived values enter a vulnerable toll/backend API; secure mode contrasts parameterized queries and server-side authorization.
Reverse engineering
Decoder, firmware and packet formats require learners to recover fields, checks, hidden states and control paths.
Binary exploitation
Synthetic parser targets cover length mismatch, unsafe copy, format logging and controlled local success effects.
Hardware security
HDL state machines, bitstream logic and frequency-routing flaws connect cyber control to physical decisions.
The harder levels should combine domains: cryptographically valid but stale packets, memory-safe but authorization-broken parsers, and RF events that become software input.

## Slide 8
The advanced end should feel like current contested-spectrum practice
The project’s stretch goal is not just harder puzzles; it is layered security thinking across hardware, propagation, jamming, cyber and detection.
SIGNAL FORGE CTF
08
Chart: 
| RF | Cyber | Hardware | Jamming | Detection
Current implementation | 3 | 4 | 2 | 2 | 2
SOTA target | 5 | 5 | 5 | 5 | 5
1
RF and propagation realism
Fading, Doppler, receiver dynamic range, AGC and adjacent-channel effects.
2
Jamming and deception
Spot, barrage, sweep, follower, replay and protocol-aware interference.
3
Hardware trust
Secure boot, signed firmware, key separation, attestation and HDL review.
4
Fusion and anomaly detection
RF features, protocol state, backend logs and operator effects correlated together.

## Slide 9
Evidence and testing turn the concept into an assessable project
The project now has a requirements spreadsheet, structured task data, local validation, and repeatable signal generation hooks.
SIGNAL FORGE CTF
09
Evidence package
Spreadsheet maps subtasks, flag location and evidence
Contexts and challenges are generated into JSON
Flags validate server-side, not in browser source
GNU Radio task replays stem from generated scripts
Guide page explains WSL, ZMQ and external signal feed
Test focus
All challenge pages render without leaked answers
Waterfall, cursors, zoom and pause/play work
Script terminal can receive, tune, interfere and transmit
Attack mode succeeds where secure mode rejects
Raw IQ and live SSE endpoints remain bounded

## Slide 10
The next build should convert the outline into a serious training range
The bones are in place. The highest-value work is adding richer signal schemes, stronger local binaries, and a clearer assessor-facing evidence trail.
SIGNAL FORGE CTF
10
1
Unique signal per context
Move beyond repeated ASK/OOK into FSK, hopping audio, DSSS-like spreading, replay and jamming classifiers.
2
Hard cyber artifacts
Build stripped binaries, firmware images, fuzz harnesses and safe patched comparisons.
3
Operational effects
Make signs, consoles, warning lights, relay nodes and gates visibly react to solved tasks.
4
Assessment polish
Keep answers server-side, write solver notes, and preserve a requirements-to-evidence matrix.
A strong final version teaches people to think like RF operators and cyber defenders at the same time.